## Slide 1: TNC MCU Project Basics
Kobe K., David Cain, and Kaleb Leon

## Slide 2: What is a TNC? (Terminal Node Controller)
A device used by amateur radio operators to participate in AX.25 packet radio networks, with the addition of a modem to convert baseband digital signals to audio tones.

## Slide 3: How packets are formatted (PC to TNC)

## Slide 4: KISS Mode
Packet format from PC to TNC or vice versa. Containing a start and end flag with a payload in the middle. (Assuming those flags will be considered our PTT?)
C0 | PAYLOAD | C0

## Slide 5: How packets are formatted (TNC to TNC)

## Slide 6: HDLC (High level Data Link Control)
Flags (start and end) – 01111110
Address – AX.25
Control – What is the data? Information, number, unnumbered, or supervisory
Information – Basically your data up to 256 octets(512 bytes)
FCS(aka Parity Bits) – used for error checking, a set of bits defined at the transmission side from the other frames using algorithm. If not the same on the received side packet is discarded.

## Slide 7: AX.25 Protocol
Specifies that the address field of the HDLC frame be split into multiple addresses:
Source Address
Zero or more repeater addresses
Destination Address
Addresses correspond to stations call signs

## Slide 8: Level ZERO Diagram
Audio Tone (Frequency may vary)
Bit Stream
Audio Tone (Frequency may vary)
Bit Stream
TNC MCU
From PC
To PC
From Radio
To Radio

## Slide 9: Scope of Work

## Slide 10: System Basic Functionality
Receiving
Receive Audio Tone Signal
Analog to digital convert into binary
Gather payload
Check for Errors
Send payload via KISS to PC
Transmitting
Receive KISS formatted data from PC
Follow AX.25 protocol to form data packet
Translate into analog audio tone signal
Send Audio tone to radio

## Slide 11: Specs

## Slide 12
Stuff | Requirements
Power | 3.3 VDC to 5.5 VDC 10 mA
Environmental | -30 to 70 deg C <2x2 Inches
Audio Input | 50 mV into 1K ohms BER 10-3 @ 6db snr
Audio Output | 400 mV into 1K ohms
Protocol | KISS Mode AX.25 HDLC
Digital Input | 3 Volt UART
Digital Output | 3 Volt UART
LED Indicators | PTT indicator RX good Packet Energy in Audio Passband
PTT (Push to Talk) | Active High & Low Supply and Sink 20 mA Accept 3 to 15 Volts

## Slide 13: By When?
By the end of the year

## Slide 14: Questions

## Slide 15
PTT – Physical or Digital? Will the 3 to 15 Volts be sent from the controller to the radio to turn on transmission?
Audio Input/output – Is the 1 Kohm load on the radio side?
UART Interface – USB port maybe?
Meetings on Tuesdays?